## Slide 1: Base Camp Water System Diagramming Tool
Version 1.0
17 May 2023
Force Health Protection personnel use this tool to illustrate and summarize the design of a base camp water system. Base camp water system diagrams are useful for communicating the design and facilitating documentation within systems of record. Also, a water system diagram is a useful way to begin the development of a sampling and analysis plan.
Note: Base camps are either contingency locations or enduring locations that do not have a robust water system program.

## Slide 2: Instructions
(1) What to Do
Develop your water system diagram on Slide 4 by using the icons and common modifiers from Slide 3. If completing a diagram on a computer, then icons can also be found in the area surrounding Slide 4.
The diagramming conventions and common modifiers are not mandatory, they can be altered if the user can annotate the diagram to clarify its meaning.
More than one water system can be displayed if desired. Add notes to Slide 4 if needed to provide clarity.
On Slide 4, the light green table should be completed by the individual drawing the diagram. The dark green table is to be filled in if the diagrammed water system(s) have identification numbers within DOEHRS-IH.
(2) Example Diagrams
There are example water system diagrams starting on Slide 5.
These examples are designed to illustrate diagramming methods and don’t necessarily reflect real situations nor provide all possible configurations. However, they should be helpful for how situations can be illustrated.

## Slide 3: Icons and Modifiers
Do not delete or modify any of the icons and modifiers on this slide. To use them, simply copy and paste each one you need into Slide 4. Then, on Slide 4, update them as necessary for your site-specific diagram. For your site-specific diagram, replace each icon’s MOD with a specific modifier. If a common modifier does not apply to a situation, then use OTH (Other) or generate your own modifier label and explain in your diagram.
MOD
Untreated water source
MOD
Treated water source
Water Source*
Treatment
Water Container*
MOD
Point of Use (POU)*
MOD
MOD
Multiple Units*
Field Test with AWT Sample
Common Modifiers (MOD)
GW – Groundwater
MW – Municipal Water
SW – Surface Water
MOD
Treated water container
Common Modifiers (MOD)
MFWPS – Military Field Water Purification System
COTS – Commercial/Non-fielded small purification system
CTR – Contractor-Built System
WTP – Fixed Water Treatment Plant
DIS – Disinfection only
(a DOEHRS component if mechanical dosing)
Common Modifiers (MOD)
BUF – Water Trailer (Buffalo)
CAM – Water Trailer (Camel)
COM – Commercial Tank
FB – Fabric Tank/ Bladder
HIP – Water Tank Rack (Hippo)**
TR – Commercial Tank Truck/ Trailer
** Within DOEHRS-IH, a Water Tank Rack (Hippo)
is called a Water Tank Truck MILSPEC
Common Modifiers (MOD)
A – Alloy
ACP – Asbestos Cement Pipe
C – Canvas
CI – Cast Iron
CN – Copper/Nickel
GS – Galvanized Steel
PVC – Polyvinyl Chloride
UNK - Unknown
Common Modifiers (MOD)
AS – Aid Station/ Medical Facility
BK – Barracks
DFAC – Dining Facility
L – Laundry
LT – Latrine
OPS – Operational building
R – Recreation
SH – Shower
WP – Water Point
WR - Washrack
Distribution System
Mobile Delivery***
Pipe / Hose
Sampling Point
*** No MOD needed for the dashed line
Multiple Units*
MOD
Treatment system
Note: Provide brief system description
Water Quality Categories:
Untreated
Treated
Disinfected
Field Test Only
Note: MW – Municipal Water should be annotated as ‘untreated’ per TB MED 577 (Section 2-3). Water from host nation municipal drinking water systems is non-potable until shown to meet appropriate MFWS, and/or is approved by PM personnel for drinking.
MOD
Untreated water container
MOD
MOD
* Source, Container, POU icons can be multiples
Multiple Units*
MOD
MOD
MOD
Disinfected fresh water container
DIS
Disinfection only
MOD
Disinfected fresh water source

## Slide 4: Base Camp Water System Diagram
Completion Date | Country: | 
 | Base Camp: | 
Preparer’s Name, Email, Unit: |  | 
Disinfected
Water Quality:
Untreated
Treated
DOEHRS-IH Water System (WS) Information | 
WS ID | WS Name
MOD
Untreated water source
MOD
Disinfected fresh water source
MOD
Treated water source
MOD
Multiple Units
MOD
Treated water
container
MOD
Treatment system
Field Test with AWT Sample
Field Test Only
Multiple Units
MOD
Multiple Units
MOD
Point of Use
DIS
Disinfection only
MOD
Untreated water
container
MOD
Disinfected fresh
water container
Multiple Units
MOD
MOD
Multiple Units
Multiple Units
MOD
MOD
MOD
MOD

## Slide 5: Example Diagrams

## Slide 6: Example Water System Diagram #1
GW
Patriot – Well #2
Spigot
TR
Tank Truck SN:
1234GY
COM
Patriot – Tank #1
SH
Shower Trailer #1
Tap1
L
Force Provider
Laundry #1
Tap1
A
PVC
The diagram quickly communicates the key aspects of the design and uses of the water system. This diagram has two systems.
It includes all water system components and points of use; and depicts how water moves from the source to all points of use.
The water system component icons (triangles, diamonds, circles, and boxes) should reflect whether the water at that point in the system is treated water, disinfected fresh water, or untreated water.
Example sampling points are shown here; note that these will be needed when creating a sampling and analysis plan (SAP).
TWPS
PAT – TPWS
SN: 0YT763
PVC
DFAC
Patriot DFAC
PVC
Veggie Sink
Effluent
Note about sampling points
Adding sampling points is optional. When creating your water system diagram, do not add sampling points until the diagram is accurate. Then, add sampling points only if desired to communicate planned or actual sampling activities. Specific sampling point selection guidance is currently being developed.
Water System 1
Water System 2
Disinfected
Water Quality:
Untreated
Treated

## Slide 7: Example Water System Diagram #2
ROWPU
ROWPU
Water System 2
GW
Alpha Well #1
BK
DFAC
Water System 1
Base Camp Boundary
Commentary
While there is one diagram here, for the purposes of DOEHRS-IH documentation there are two (2) water systems at the base camp. Both systems share the same source of water, a ground water well. Note that both water systems can be drawn together as shown here, and that in this example all elements of both water systems are physically located within the boundaries of the base camp. Also, note within water system 1, how to show a water container being used directly next to a point of use.
BUF
Water Buffalo
AS
Disinfected
Water Quality:
Untreated
Treated
Note:
Adding base camp and water system boundaries to a diagram is optional. They have been added in this series of examples in order to facilitate discussion.
SH-LT
3 units
COM
Disinfected fresh
water container

## Slide 8: Example Water System Diagram #3
Commentary
In this example, there is one water system and the water source for the system is located outside the boundary of the base camp. Note that how the water gets from the river to the two ROWPU units is via a pipe or hose, since the connecting lines are solid.
ROWPU
ROWPU
SW
Meade River
SH-LT
2 units
BK
DFAC
ROWPU
ROWPU
COM
Treated water
container
Base Camp Boundary
Water System
Disinfected
Water Quality:
Untreated
Treated

## Slide 9: Example Water System Diagram #4
Commentary
Here, there are two (2) nearby base camps and each camp has its own water system. However, both water systems share the same water source, a local host nation municipal water system, which derives from a local river.
Note: For DOEHRS purposes, each base camp could have its own separate diagram. They are combined here for illustration and discussion.
ROWPU
ROWPU
SH-LT
4 units
MW
Host Nation
Municipal Water System
SW
River
Base Camp B
Base Camp A
Water System A
Water System B
DFAC
BK
Disinfected
Water Quality:
Untreated
Treated

## Slide 10: Example Water System Diagram #5
Commentary
This illustrates a case where our base camp sits within a host nation’s military base. Note that the host nation’s water treatment system is rendered using a triangle with an “X” even if they treat their water. This is because U.S. field water doctrine states that, in general, any water source must be U.S. treated before we use it ourselves no matter how that source water is treated. The exception to this is when source water is approved by the local US medical authority or is provided and treated by a NATO ally and meets standards in STANAG 2136 (refer to TB MED 577).
SW
Lake Zulu
MW
Host Military’s
Water Treatment System
TR
Disinfected fresh
water container
U.S. Base Camp
U.S. Base Camp Water System
Host Nation’s Military Base
DFAC
BK
Disinfected
Water Quality:
Untreated
Treated

## Slide 11: Example Water System Diagram #6
Commentary
Here is a situation where one base camp receives its source water from another nearby base camp via a Tank Truck, which transports water from one camp to the other. Note that the water system for Base Camp B includes the Base Camp A treatment system and the source water from that system, because all water system diagrams must show the origin of the water prior to U.S. military treatment.
ROWPU
Treatment System
TR
BK
2 buildings
w/ showers
MW
Untreated water source
SW
Untreated water source
SH
5 trailers
Base Camp B
Base Camp A
Base Camp B Water System
Base Camp A Water System
Disinfected
Water Quality:
Untreated
Treated

## Slide 12: Example Water System Diagram #7
Commentary
Yes, three water systems can be shown on one diagram, this one shows three (3). All three source their water from a host nation municipal water system.
MW
OPS
6 buildings
(operations)
ROWPU
LSA
4 buildings
ROWPU
Base Camp
Boundary
Water System 1
Water System 2
Water System 3
Host Nation
OPS
10 buildings
Disinfected
Water Quality:
Untreated
Treated

## Slide 13: Example Water System Diagram #8 (Team House)
Commentary
The diagramming tool can also be used for team houses. In this example, within a team house there are multiple points of use, in the kitchen and the bathroom, and the water container is also part of the team house.
MW
Untreated (unknown treatment)
municipal water source
Aspen 1800BC
Treatment system
SH
Team House Shower
L
Team House Latrine
KITCH
Team House Kitchen
Team House
Disinfected
Water Quality:
Untreated
Treated
COM

## Slide 14: Example Water System Diagram #9 (Team House)
Commentary
In this team house example, a tank truck delivers host nation municipal water to a commercial water tank that is part of a team house. Within the house there are distribution pipes from the water tank to the kitchen and the bathroom. Within the bathroom, there are multiple points of use, a latrine, a shower, and a utility sink
MW
Untreated (unknown treatment)
municipal water source
TR
Tank Truck
COM
Water Tank
BATH
Bathroom
(Latrine, Shower, Utility sink)
KITCH
Team House Kitchen
Team House
Disinfected
Water Quality:
Untreated
Treated